## Slide 1: Clustering of energy consumption time-series data

## Slide 2: Clustering
using Python package – tslearn
algorithm used – K-means (method)
using Euclidean metrics (if results are not satisfying might be changed)
10 cluster (chosen as optimal when the steepest decrease of variance is observed)
unique pairs (user_ID, day) in clusters
calculation of frequency of occurrences of pair with specific user_ID in all clusters
cluster for user_ID – is chosen as the one with for which the frequency of occurrence is the highest

## Slide 3: Preprocessing data
GasDataWeek_.csv
  data for 3 months(31.12.2009-1.3.2010) (GasDataWeek0.csv-GasDataWeek13.csv)
  energy consumption in every 30 minutes
Residential allocations
  chosen IDs for users in control group (543 IDs)
Smart meters Residential pre-trial survey data – Gas.csv
  answer of survey for each ID

## Slide 4: Results
pre-trial survey data sorted due to assignment to clusters into 8 files: pre-trial survey-cluster_0.csv….. pre-trial survey-cluster_7.csv
energy consumption profiles with centroid profile for every cluster:

## Slide 5: Results
using frequency tables for analysis!!!!-should try – write separate script for the analysis of final.csv file
http://hamelg.blogspot.com/2015/11/python-for-data-analysis-part-19_17.html

## Slide 6: Clustering of average profile
days in period 1.12.2009 – 21.12.2009 and 5.1.2010-1.3.2010 without weekends taken and averaged for every ID

## Slide 7: Notes from evaluation average profile clustering with normalization
retired people in different clusters than working
people with at least one child – almost always in cluster with peak in the morning! while among working people they might have only small peak in the morning or none
results seems to be better without setting maximum
using only control group of people – people in poverty can be distinguished (very small number!) – doesn’t help adding 1,2,3 group of people (might be problem with normalization?)

## Slide 8: What else can be done?
If the results are not satisfying:
  different metric/period
  different approach:
    for every ID count average profile in derides period (3 months)
    cluster average profiles